# olpc-radio-testing
## test scripts howto
15:17 12th February 2007, by James Cameron
### logging in and initialising environment
The test scripts are kept separate from the installed software, in a subdirectory olpc-radio-testing in the olpc username. An /etc/profile.d script sets up the PATH environment variable so that the test scripts are available as commands in any shell.
### test setup commands
nm-down

turns off normal managed network mode. do this before adhoc-up.

adhoc-up

reconfigures wireless network interface for ad-hoc network between two units, usually units 1 and 3. use nm-down first.

adhoc-down

turns off wireless network adhoc mode.

nm-up

reconfigures wireless for managed network mode against access point.
### test run commands
battery-monitor

every second logs battery and temperature to screen and tail of file battery-monitor.log

battery-watch

every minute logs battery to screen and battery.log

walkabout

every second logs `battery-temperature` `ambient-temperature` `battery-capacity` `signal-level` `noise-level` `ping-time` to screen and walkabout.log

af

emit beep every half second to indicate signal strength.

af-ping

emit signal strength beep on every returned ping

adhoc-retune-sequence

try every channel and generate statistics per channel (lacks analysis scripts)]

### remote access

shell

ssh root@quozl-1

file system

konqueror fish://root@quozl-1/